Ανάπτυξη εφαρμογής Αυθαίρετων Συναρτήσεων
(Arbitrary Waveform Generator) σε πλατφόρμα Arduino

---
Περιεχόμενα
01
Ανάλυση προβλήματος
02
Arduino και γεννήτριες τυχαίων κυματομορφών
03
Απαιτήσεις λογισμικού
Απαιτήσεις hardware και συνδεσμολογία
04
05
Πλατφόρμα ανάπτυξης και προσομοίωση
06
Λειτουργία

---
01
Ανάλυση προβλήματος
Γεννήτρια τυχαίων κυματομορφών
Υλικά
Επικοινωνία των εξαρτημάτων
Ανάπτυξη λογισμικού
Συνδεσμολογία
Λειτουργικότητα

---
02
Massimo Banzi, David Cuartielles, Tom Igoe, Gianluca Martino και David Mellis
2005 Italy
The first Arduino board, the Arduino NG
Uno, Mega, Nano, Due, Pro Mini, Leonardo,MKR series, Zero, Gemma, LidyPad
Μικροελεγκτής ανοιχτού κώδικα
Arduino IDE
Arduino

---
02
Γεννήτρια τυχαίων συχνοτήτων
Δημιουργία custom σημάτων
Επεξεργασία σήματος
Υψηλή ακρίβια σήματος
Μεγάλο εύρος συχνοτήτων
Πολλαπλά κανάλια σημάτων
Επεξεργασία τυχαίων σημάτων
Test ηλεκτρονικών κυκλωμάτων
Test RF και Wireless
Επιστημονική έρευνα
Ανάπτυξη προϊόντων
Ιατρική χρήση
Αεροδιαστιμική και άμυνα
Τεστ ήχου

---
03
Απαιτήσεις λογισμικού
Θα διαθέτει οθόνη touch στην οποία θα υλοποιηθεί γραφικό περιβάλλον.
Θα μπορεί να παράγει ημιτονοειδείς, τριγωνικές, πριονωτές και τετραγωνικές καθοριζόμενης συχνότητας και πλάτους.
Θα εμφανίζει στην οθόνη την μορφή της κυματομορφής όπως και τα χαρακτηριστικά της(συχνότητα και πλάτος).
Θα διαθέτει επιλογή σύνθεσης κυματομορφής απο τον χρήστη και την οποία θα αποθηκεύει στην εσωτερική EEPROM του Arduino.
Θα εξάγει την σχεδιασμένη κυματομορφή και ταυτόχρονα θα την εμφανίζει στην οθόνη.
Θα διαθέτει την δυνατότη φόρτωσης(load) της αποθηκευμένης κυματομορφής που σχεδίασε ο χρήστης αλλά και επιλογή διαγραφής.

---
04
Arduino Mega
Nextion NX8048T050
DAQ MCP4725 12bit
5V supply
Καλώδια
[Speaker Notes: ΑΠΑΙΤΗΣΕΙΣ HARDWARE ΚΑΙ ΣΥΝΔΕΣΜΟΛΟΓΙΑΣ]

---
04
Συνδεσμολογία κυκλώματος

---
04

---
05
Arduino IDE
Nextion Editor

---
05
Arduino IDE

---
05
Nextion Editor

---
Create new

---
Load existing

---
Load existing

---
EEPROM

---
Nextion
sends va0
variable
Arduino asks
for va0
variable
ARDUINO MEGA
home page and loading page
input for sine signal
create sine signal
input for triangle signal
create triangle signal
input for square signal
create square signal
input for sawtooth signal
create sawtooth signal
input for custom signal
calculations for custom signal
create custom signal
check EEPRO for signals, delete or load signals
save custom signal on available memory slot
load saved signal
NEXTION DISPLAY
va0 = 0
va0 = 11
va0 = 1
va0 = 12
va0 = 2
va0 = 13
va0 = 3
va0 = 14
va0 = 4
va0 = 5
va0 = 6
va0 = 7
va0 = 8
va0 = 9
va0 = 10

---
home page and loading page
ARDUINO MEGA
Initialize variables
va0=5
va0=0
va0=8
is
va0 = 0?
yes
no
6
execute loop according to va0 value
va0=11
va0=12
va0=13
va0=14
va0=0
va0 = 0
NEXTION DISPLAY

---
input and production of sine signal
ARDUINO MEGA
ARDUINO MEGA
get amplitude, frequency, duration,
calculate signal and send info in Nextion
change by home
or back button
is
va0 = 11?
yes
no
va0 = 0
va0=0
va0=0
change by create button
no
va0 = 1
ARDUINO MEGA
produce wave for x duration
change by home
or back button
is
va0 = 11?
yes
va0 = 0 or
va0 = 11
no
va0=0
va0=0
va0 = 1
va0 = 11
NEXTION DISPLAY

---
input and production of triangle signal
ARDUINO MEGA
ARDUINO MEGA
get amplitude, frequency, duration,
calculate signal and send info in Nextion
change by home
or back button
is
va0 = 12?
yes
no
va0 = 0
va0=0
va0=0
change by create button
no
va0 = 2
ARDUINO MEGA
produce wave for x duration
change by home
or back button
is
va0 = 12?
yes
va0 = 0 or
va0 = 12
no
va0=0
va0=0
va0 = 2
NEXTION DISPLAY
va0 = 12

---
input and production of square signal
ARDUINO MEGA
ARDUINO MEGA
get amplitude, frequency, duration,
calculate signal and send info in Nextion
change by home
or back button
is
va0 = 13?
yes
no
va0 = 0
va0=0
va0=0
change by create button
no
va0 = 3
ARDUINO MEGA
produce wave for x duration
change by home
or back button
is
va0 = 13?
yes
va0 = 0 or
va0 = 13
no
va0=0
va0=0
NEXTION DISPLAY
va0 = 3
va0 = 13

---
input and production of sawtooth signal
ARDUINO MEGA
ARDUINO MEGA
get amplitude, frequency, duration,
calculate signal and send info in Nextion
change by home
or back button
is
va0 = 14?
yes
no
va0 = 0
va0=0
va0=0
change by create button
no
va0 = 4
ARDUINO MEGA
produce wave for x duration
change by home
or back button
is
va0 = 14?
yes
va0 = 0 or
va0 = 14
no
va0=0
va0=0
NEXTION DISPLAY
va0 = 4
va0 = 14

---
create custom wave
ARDUINO MEGA
va0=0
va0=0
va0=6
va0=0
va0=5
va0 = 6
va0 = 7
va0 = 9

---
ARDUINO MEGA
choose signal resolution and create your signal,
nextion sends data to arduino and calculates signal
change by home
button
Save signal in EEPROM
and go to homepage
is
va0 = 5?
yes
no
va0 = 0
change by preview button
no
va0 = 6
ARDUINO MEGA
change by home button
ARDUINO MEGA
va0 = 0
change by save button
va0 = 9
no
no
preview wave and choose frequency
no
preview wave and choose frequency
is
va0 = 7?
yes
no
change by create button
va0 = 7
is
va0 = 6?
yes
no
ARDUINO MEGA
produce wave for x duration
va0 = 14
va0 = 0
change by back button
no
change by home button
NEXTION DISPLAY
va0 = 5

---
EEPROM
ARDUINO MEGA
ARDUINO MEGA
check for saved signals, if yes enable buttons
check for delete variables, if yes delete signals
check for load variables, if yes load signals
change by back button
is
va0 = 8?
yes
no
va0 = 0
va0=0
change by load button
no
va0 = 10
ARDUINO MEGA
load signal, send info to Nextion
produce signal
change by
back button
va0=8
is
va0 = 10?
yes
va0 = 8
no
va0 = 10
NEXTION DISPLAY
va0 = 8

---
Libraries
Signal resolution
void sinewave16t()
void sinewave8()
void triangle8()
void pulse2()
void sawtooth5()
void customwave() 2-20
#include <Adafruit_MCP4725.h> //Library για DAC MCP4725
#include <Wire.h> //I2C Library επικοινωνίας
#include "EasyNextionLibrary.h" //Nextion Library
#include <EEPROM.h> //EEPROM library